## Slide 1
Name: Deepak Kumar
Designation: Trainee (Internship)
Institution: National Institute of Technology, Agartala
Project Title: FPGA-Controlled Infrared Imaging System
MAJOR OBJECTIVES:
PHOTO
METHODOLOGY FLOW CHART:
RESULTS/MAJOR FINDINGS:
CONCLUSION:
Guide: Dr. Sandip Paul
Contact e-mail: san@sac.isro.gov.in
20 Jan 2025 to
7 July 2025
SRTD-RTMG-MISA
Bias and Power Supply Design RHFL4913A LDOs 9 Voltages
IR Detector (ULIS 03 19 1 Micro-bolometer)
Clock & Control Signal Generation (Using FPGA: MC, INT, RESET, SERDAT)
Detector Data Capture & Demultiplex (12-bit Pixel from 6-bit Bus)
Temperature controlled electronics card Setup
To develop an infrared imaging system using the ULIS 03 19 1 micro-bolometer. To design FPGA logic for synchronized control signal generation(RESET, INT, SERDAT, MC) and pixel data acquisition. Developing of Temperature Controlled Electronics Card for controlling detector internal temperature.
1. All nine detector biasing voltages were successfully generated using RHFL4913A LDOs.
2. FPGA logic (VHDL) was successfully implemented for detector interfacing and timing control.
3. Four key clocks—RESET, INT, MC, and SERDAT—were generated with precise synchronization.
4. Successfully captured detector data and reconstructed it into 12-bit per pixel thermal frames.
5. Made Setup of Temperature Control Card using MAX1978 IC for controlling Detector TEC.
The FPGA-controlled infrared imaging system was successfully implemented with verified biasing, clock generation, and 12-bit pixel reconstruction logic. The temperature-controlled electronics card for the detector is ready, and the system is prepared for the next stage of offline image reconstruction